## Slide 1: EE-694 : Seminar Improving the Performance and Energy Efficiency of Asymmetric Multicore System
Computer Architecture & Dependable Systems Laboratory,
Department of Electrical Engineering, Indian Institute of Technology Bombay
Presenter: Siddhant Singh Tomar
Roll No.: 213079010
Supervisor: Prof. Virendra Singh

## Slide 2: Outline
Introduction
Motivation
Literature Survey:
- Improving Single Thread Performance
- Reducing Switching Overhead
- Increasing Dynamic Adaptability of a Asymmetric multicore system.
Conclusion

## Slide 3: Introduction
Notes: Increase freq while proportionally scaling down voltages

## Slide 4: Symmetric CMPs vs Asymmetric CMPs
Symmetric CMPs (All Big OoO cores) | Symmetric CMPs (All Small InO cores) | Asymmetric CMPs (Few big and multiple small cores)
Low throughput | High throughput | Avg. throughput
Best single thread performance | Poor Single thread performance | Good single thread performance
Power hungry cores | Power efficient cores | Best of both

## Slide 5: ARM’s big.LITTLE
Cortex-A15 is a 3-way out-of-order (OoO) core (15-25 stages).
Cortex-A7 is a narrow 2-way in-order (InO) core (8-10 stages).

## Slide 6: Opportunities for Improvement
Switching
Overhead
  Single Thread
  Performance
Dynamic Adaptability

## Slide 7
Single Thread Performance

## Slide 8: Run-Ahead Execution
Younger instructions cannot be executed.
ADD R2  R2, 64
LOAD R2 mem[R5]
ADD R4  R4, R5
MUL R4  R4, R3
LOAD R3  mem[R2]
ADD R2  R2, 8
ADD R7, R1, R2
LOAD R1  mem[R5]
Small instruction Window: Full window stalls
(8-instruction ROB)
LLC Miss! Takes 80-100 of cycles
LOAD R3  mem[R7]
Remove the Blocking instruction from the head of ROB.
If instruction is a long latency cache miss: =>Checkpoint ARF and enter Run-ahead mode
Run-Ahead mode:
Pre-execute instructions for prefetching purposes.
Cache-miss dependent instructions are marked invalid and dropped.
When Original miss returns=>restore checkpoint=>flush pipeline=>resume normal execution
Head:
Notes: When the ROB becomes full instruction dispatching needs to be stalled, ROB can become full if oldest instr. is a long latency cache miss

## Slide 9: Run-Ahead Execution (contd..)
Without Runahead:

## Slide 10: Limitations of Run-Ahead Execution
Reorder Buffer (ROB), Reservations station (issue queue) and physical register file is freed.
All the instructions executed in Run-Ahead mode needs to be re-executed in normal mode.
Poor performance in pointer chasing application.(Load dependent load instructions)
Notes: State of ROB,RS and PRF rendered useless

## Slide 11: Precise Run-Ahead (PRE)
PRE does not release processor state when entering runahead mode.
PRE leverages the available issue queue and physical register file entries to speculatively execute instructions in Run-ahead mode.
Key observations:
-37% of the issue queue entries
-51% of the integer registers
-59% of the floating-point registers are free.

## Slide 12: Processor Pipeline For PRE
Precise Run-ahead execution improves the IPC by 38.2% over the baseline.

## Slide 13: Limitations of Precise Runahead
Poor performance in pointer chasing application and for complex indirection patterns.(Load dependent load instructions)

## Slide 14: Vector Runahead
ADD edx, edx, ecx
MOV ecx, dword ptr[ebx]
MOV ebx, dword ptr[eax]
XOR eax,0x12345678
ADD rax,0x04
MOV eax, dword ptr[rax]
VADDPD zmm3,zmm3,zmm2
VGATHERDPD zmm2, zmm1
VGATHERDPD zmm1, zmm0
VXORUPD zmm0,0x12345678
VMOVUPD zmm0,zmmword ptr [rax*4]
One loop iteration
(scalar instructions)
Eight Loop iterations
(x86-AVX-512 SIMD
instructions)
(Vectorizing load slice)
Striding load instruction
Notes: VA prefetch entire load chains across multiple iterations, using vector or SIMD instructions………………….explain slide…….issue batch of mem. Access to A

## Slide 15: Processor Pipeline for Vector Runahead
Stride detector => Produce vector load instruction for striding load
Taint vector => Track instructions dependent on vector load
Address generating scalar instructions  vector unit operations
Dependent Loads  vector gathers

## Slide 16: Limitations of Vector Runahead
Complex control flow limits the ability of Vector Runahead to cover enough of the application’s memory accesses
Vector Run-ahead stays in “Run-ahead” mode for longer duration, can prefetch data from wrong path due to branch divergence, incurring more penalty.

## Slide 17
Reducing Switching Overhead

## Slide 18: Composite core
Composite core achieves 18% energy efficiency over execution on only big core, while limiting performance to 5% loss.

## Slide 19: Limitations of Composite Core
On an average of only 25% of the dynamic execution is mapped to the little uEngine
little uEngine adds an additional 20 % area overhead

## Slide 20: Dynamic schedule Migration for heterogenous cores (DynaMOS)
Out-of-Order (OoO) cores creates optimized issue schedules of instructions
Offload recurring issue schedule from big to little core
DynaMOS is able to run 37% of its instructions on little.
DynaMOS achieves energy savings of 32% over execution on only big core, with an allowable 5% performance loss

## Slide 21: Limitations of DynaMOS
Renaming of architectural register is limited to at most 4 physical registers =>discard schedules, limiting achievable energy savings.
Size of physical register file is 4 times as compared to simple in order core.

## Slide 22
Dynamic Asymmetric multicore system

## Slide 23: MorphCore
“MorphCore” micro-architecture can handle single threaded code at high performance, and multi-threaded code at high throughput.
It provides two modes of execution: => 2-way SMT out-of-order core mode. => 8-way SMT in-order core.
Notes: MorphCore exposes 8 logical cores to OS.

## Slide 24: The MorphCore Microarchitecture

## Slide 25: Limitation of MorphCore
Poor performance for multithreaded applications which have more no. of critical sections.
.

## Slide 26: Illusionist
A large number of lightweight cores by get execution hints from an aggressive core.
A just-in-time compiler analysis for program distillation
A predictor for identifying the phases of program execution that benefit most from execution hints.

## Slide 27: Aggressive and lightweight core working together

## Slide 28: Limitations of Illusionist
PC, age tag and release window metric are sent along with the branch outcome to LWC
=> Increasing Branch Outcome Queue (BOQ) sizes.
=> Not enough to guarantee perfect timing for hints utilization.

## Slide 29: R3-DLA : Decoupled Look Ahead Execution
On top of this basic design, we propose to add a number of supporting elements to accelerate main thread (MT) as well as reduce the size of lookahead thread (LT):
Reduce : T1, A prefetching FSM to offload prefetching of loop based strided accesses
Reuse : logic to pass register values from LT through FQ and used as predictions in the front-end of MT
Recycle: cycles through a number of skeleton mask bits to pick the best performing configuration

## Slide 30: Illusionist vs R3-DLA
Idea | Size of look ahead thread | Utilization of Branch hints | Utilization of Other hints | Branch Alignment
Illusionist | 25% of the main thread. | PC, Age tag, release window. | Age tag, release window. | Preserving PC in LT
R3-DLA | 20% of the main thread. | Only branch outcome. | Dequeue with branch outcome. | No branches removed in LT

## Slide 31: Conclusion
Single Thread Performance:
Run-Ahead execution generates highly accurate prefetches, which increases the IPC at the expense of executing more no. instructions.
Reducing The Switching Overhead:
Composite Core minimizes switching overhead to enable fine grained switching,But the little uEngine incurs an additional overhead of 20%.
DynaMOS builds on the work of composite core to increase utilization of little core, but little core requires additional hardware to run in OinO mode.

## Slide 32: Conclusion (contd..)
Dynamic Adaptability:
MorphCore is more energy-efficient than a traditional out order core when executing multi-threaded programs
Illusionist, dynamically adapts to workloads ,providing the performance of a symmetric multicore system with all big cores while consuming energy equivalent to that of little cores
R3-DLA improves the single thread performance. But compiler support is needed to generate skeleton mask bits and identifying strided instructions

## Slide 33: References
O. Mutlu, J. Stark, C. Wilkerson and Y. N. Patt, "Runahead execution: an alternative to very large instruction windows for out-of-order processors," The Ninth International Symposium on High-Performance Computer Architecture, 2003. HPCA-9 2003. Proceedings., 2003, pp. 129-140, doi: 10.1109/HPCA.2003.1183532.
A. Naithani, J. Feliu, A. Adileh and L. Eeckhout, "Precise Runahead Execution," 2020 IEEE International Symposium on High Performance Computer Architecture (HPCA), 2020, pp. 397-410, doi: 10.1109/HPCA47549.2020.00040.
Naithani, S. Ainsworth, T. M. Jones and L. Eeckhout, "Vector Runahead," 2021 ACM/IEEE 48th Annual International Symposium on Computer Architecture (ISCA), 2021, pp. 195-208, doi: 10.1109/ISCA52012.2021.00024.
A. Ansari, S. Feng, S. Gupta, J. Torrellas and S. Mahlke, "Illusionist: Transforming lightweight cores into aggressive cores on demand," 2013 IEEE 19th International Symposium on High Performance Computer Architecture (HPCA), 2013, pp. 436-447, doi: 10.1109/HPCA.2013.6522339.

## Slide 34: References continued..
A. Lukefahr et al., "Composite Cores: Pushing Heterogeneity Into a Core," 2012 45th Annual IEEE/ACM International Symposium on Microarchitecture, 2012, pp. 317-328, doi: 10.1109/MICRO.2012.37.
S. Padmanabha, A. Lukefahr, R. Das and S. Mahlke, "DynaMOS: Dynamic schedule migration for heterogeneous cores," 2015 48th Annual IEEE/ACM International Symposium on Microarchitecture (MICRO), 2015, pp. 322-333, doi: 10.1145/2830772.2830791.
Khubaib, M. A. Suleman, M. Hashemi, C. Wilkerson and Y. N. Patt, "MorphCore: An Energy-Efficient Microarchitecture for High Performance ILP and High Throughput TLP," 2012 45th Annual IEEE/ACM International Symposium on Microarchitecture, 2012, pp. 305-316, doi: 10.1109/MICRO.2012.36.
S. Kondguli and M. Huang, "R3-DLA (Reduce, Reuse, Recycle): A More Efficient Approach to Decoupled Look-Ahead Architectures," 2019 IEEE International Symposium on High Performance Computer Architecture (HPCA), 2019, pp. 533-544, doi: 10.1109/HPCA.2019.00064.

## Slide 35
Thank You!